| Name | Score |
| --- | --- |
| School |  |

2009 Ag Tech Contest/FFA Ag Mech Qualifying Event

Machine and Equipment Systems

Problem:

In any plant production system, it is necessary to have available equipment, which can be used for multiple functions.  Utility vehicles fall into this category of equipment.  These units are used on a daily basis and require timely maintenance and repair.

A producer has a John Deer Gator, which requires the replacement of the roller chains connecting the drive train and drive wheels.  When you attempt to order these roller chains from the manufacturer, you find that they are temporarily out of stock.  To get this unit repaired as soon as possible, you decide to use "stock" chain from your parts supplier.

Procedure:

You must specify the correct chain and custom make the chain to fit.

Neatness, spelling, accuracy, and penmanship are also essential in any successful service function.

- Using the data table below and a sample of chain removed from the vehicle, determine the size of the chain required to replace the original chain.

| ANSI 29.1 roller chain standard sizes |
| --- |
| Size | Pitch, in. | Roller diameter, in. | Ultimate strength, lb. | Working load, lb. |  |  |  |
| 25 | 0.250" | 0.130" | 781 | 140 |  |  |  |
| 35 | 0.375" | 0.200" | 1,758 | 480 |  |  |  |
| 41 | 0.500" | 0.306" | 1,500 | 500 |  |  |  |
| 40 | 0.500" | 0.312" | 3,125 | 810 |  |  |  |
| 50 | 0.625" | 0.400" | 4,880 | 1,430 |  |  |  |
| 60 | 0.750" | 0.469" | 7,030 | 1,980 |  |  |  |
| 80 | 1.000" | 0.625" | 12,500 | 3,300 |  |  |  |

- Record your answer in the space provided:		Size:	____________

- Using the mock-up of the chain drive assembly and tools provided at your work station, determine the

minimum length of chain, which can be used:

Minimum  Length:	_________inch

- Using the chain and tools provided at your work station:

- Cut the chain to length.

- Install the chain on the machine provided.

- Tension the chain as specified in the service manual.

| Score Sheet |
| --- |
|  | Points |
|  | Possible | Earned |
| Neatness, spelling, and penmanship | 5 |  |
| Proper specification of chain size | 5 |  |
| Accuracy of length specification | 5 |  |
| Proper installation and tensioning of chain | 5 |  |
| Safety and work habits | 5 |  |
| Total Score | 25 |  |